## Slide 1: Clinical biomechanics
Assoc. Prof. Jiří Burša, PhD.
Institute of Solid Mechanics, Mechatronics and Biomechanics
Faculty of Mechanical Engineering
Brno University of Technology
Czech Republic

## Slide 2: What is clinical biomechanics?
Biomechanics is application of knowledge, approaches and methods of mechanics to biological objects (human body – human biomechanics).
Clinical biomechanics aims at solutions to biomechanical problems required by clinical practice.
Experimental and computational methods.
Basic quantities:
Stress (force per unit area [N/m2 = Pa])
Strain (relative deformation, elongation per unit length [m/m = 1 –dimensionless quantity])
(Young’s) modulus of elasticity– stress/strain [N/m2 = Pa] – represents the material stiffness (slope of the stress-strain dependence).
Basic types of stress-strain behaviour:
Elastic (linear or non-linear) – no permanent deformation after unloading
Elastic-plastic (some portion of deformation remains permanent)
Viscoelastic (deformation is time and velocity dependent)

## Slide 3: Basic types of animal living tissues
Animal living tissues can be divided (from the mechanical viewpoint) into two basic groups:
Hard tissues (e.g. bones) – showing small strains
Soft tissues (e.g. muscles) – showing large strains
  striated muscle tissue
  smooth muscle tissue (occurs also in blood vessel walls)
Especially organs created of soft tissues show highly non-linear stress-strain dependence.
  Why is the description of large strain behaviour as difficult?

## Slide 4: Geometric nonlinearity
Geometric nonlinearity is characterized by "large" displacements and/or rotations, which can be accompanied by large strain:
  Large displacement … slender structures – fishing rod, frames, shells
  Large strain … plasticity of steels (forming simulations), .... hyperelasticity of elastomers (rubbers)

## Slide 5: Properties of arterial wall tissues
Mechanical behaviour of arterial wall tissues shows:
  structural non-homogeneity – arterial wall consists of several layers with different structure and properties, changing also in axial direction
  each layer created of several components (elastin membranes and fibres, collagen fibres, smooth muscle cells)
  large strain under physiological load
  non-linear stress-strain dependence
  viscoelasticity– time-dependent response
  anisotropy – material properties are dependent on direction
  different properties under tension or compression
  very low compressibility
  very pronounced temperature dependence of properties
  dependence on loading history
  dependence on the age of an individual
  remodelation under influence of load
  active behaviour – mechanical properties can be changed substantially by activation (or relaxation) of muscle fibres
  ...to be continued
  Many different constitutive models have been created to describe these properties.
  Hyperelastic isotropic or anisotropic models are most frequently used for modelling of soft tissues.

## Slide 6: Clinical Biomechanics
deals with human body,
solutions to biomechanical problems required by clinical practice,
solutions at the level of tissues and higher structures (organs, systems of organs, whole body)
Ilustrative problems:
Biomechanics of big joints (e.g. hip, knee, elbow joints)
  without implants (osteotomies),
  with implants (endoprostheses)
Biomechanics of vertebral column and its elements (vertebras, intervertebral plates)
Biomechanics of arteries (e.g. aneurysms, vascular grafts)
Biomechanics of fixators of lower extremities
Biomechanics of vertebral fixators

## Slide 7: Thank you for your attention